## Slide 1: RSVP Project
Telecommmunicatiesystemen
Bart Braem, Johan Bergs

## Slide 2: Example Network
BE
QoS (0.3 Mbps)
BE (1.0 Mbps)
QoS (? Mbps)
BE (? Mbps)
1.0 Mbps
Reserve resources for QoS class
+
Priority Queueing
Reserve resources for QoS class
+
Priority Queueing
1.0 Mbps
1.0 Mbps
Source
Destination

## Slide 3: RSVP
Resource ReSerVation Protocol
Some key properties
  Simplex flows
  Receiver-initiated
  Not a routing protocol, reservation signaling only
  An internet control protocol like ICMP, IGMP or routing protocol

## Slide 4: RSVP Host Model
BE
1.0 Mbps
1.0 Mbps
1.0 Mbps
PATH
RESV
Source
Destination

## Slide 5: RSVP Signaling
Succesful reservations are acknowledged by
  Confirmation messages
PATH and RESV messages
  Periodically sent along the path
  Keep alive state information
Reservations are removed by
  Explicit Teardown messages
  Soft Timers (missed K PATH messages)

## Slide 6: A simple DiffServ QoS solution
We support only 2 traffic classes
  Quality of Service
  Best Effort
Reservations
  Adds resources to the QoS class
  All sessions are mapped on the QoS class
  Session id = (DestAddr, ProtocolD, DstPort)
When a reservation is removed
  Resources are removed from the QoS class
No differentiation is made between QoS traffic

## Slide 7: QoS class in IPv4 header

## Slide 8: Result
BE
QoS (0.3 Mbps)
BE (0.7 Mbps)
QoS (0.3 Mbps)
BE (1.0 Mbps)
1.0 Mbps
1.0 Mbps
1.0 Mbps
Source
Destination